## Slide 1
PROJECT ASTRA · TECHNICAL PRESENTATION
PredictaGuard
Predictive Maintenance System for 6 Critical ASTRA Machines
Anomaly Detection · Fault Classification · Remaining Useful Life (RUL) Prediction
Turning Reactive Maintenance into Resilient Operations.

## Slide 2
01 · OPENING
Background & Urgency
In large-scale manufacturing industries, machine reliability is everything — sudden production line stoppages interrupt the flow of time-sensitive raw materials.
Currently, maintenance is still reactive or based on calendar schedules, rather than the actual machine condition.
Emergency repair costs are much higher than planned preventive maintenance.
Losses from unplanned downtime are highly significant, especially on machines at critical control points (Critical Control Points).
3×
Emergency repair costs compared to planned preventive maintenance
$100K–500K
Estimated loss per unplanned downtime incident on critical CCP machines
01
PredictaGuard · Project ASTRA

## Slide 3
01 · OPENING
Problem Statement
1
Zero Predictive Capability
6 critical ASTRA machines operate 24/7 without a predictive health monitoring system.
2
Silent Degradation
Bearings and electrical components wear out slowly without early detection until complete failure occurs.
3
Data Silo
Telemetry data (temperature, vibration, current) is already flowing, but is only stored locally without being processed into predictive insights that technicians can trust.
02
PredictaGuard · Project ASTRA

## Slide 4
01 · OPENING
Objective & Scope
Build PredictaGuard, an on-premise monitoring system with 3 main capabilities:
1
Real-Time Anomaly Detection
Identifying machine behavior that deviates from historical healthy patterns.
2
Fault Classification
Determining specific failure types: inner/outer race defect, roller fault, overload, etc.
3
Remaining Useful Life (RUL) Prediction
Estimating the machine's remaining safe operating time along with severity & action recommendations.
SCOPE
6
Critical machines monitored
(MTR-01 to MTR-06)
3
Public datasets for simulation:
Paderborn, NASA IMS, NASA CMAPSS
03
PredictaGuard · Project ASTRA

## Slide 5
02 · DATA ARCHITECTURE
Mapping 6 Machines to 3 Public Datasets
Paderborn Bearing Dataset
Conveyor · Compressor · Fan · Spindle
High-frequency vibration + motor current (MCSA) — suitable for machines with high mechanical load variations.
NASA IMS Bearing Dataset
Water Pump (MTR-04)
Gradual bearing degradation run-to-failure over weeks — ideal for slow pump wear.
NASA CMAPSS Turbofan
Mixer (MTR-05)
Multi-sensor thermal & operational cycle data, modeled as a proxy for mixer efficiency degradation.
04
PredictaGuard · Project ASTRA

## Slide 6
02 · DATA ARCHITECTURE
PostgreSQL Database Structure
motors
Basic specifications of 6 motors, safe physical limits, data sources
raw_sensor_data
Raw sensor data — without cleaning
production_context
Work shift, load level, ambient temperature
feature_windows
Statistical & spectral features per 30-second window
prediction_results
Output of 3 models + severity + SHAP explanation
WHY DOES RAW DATA ENTER WITHOUT CLEANING?
This is intentional to simulate real factory floor conditions — sensors often experience dropouts, packet loss, and noise. This approach preserves the historical audit trail while testing the robustness of the automated cleaning pipeline.
05
PredictaGuard · Project ASTRA

## Slide 7
03 · DATA PIPELINE
Multi-Format Ingestion (ETL)
1
Paderborn
.mat (MATLAB)
High-frequency vibration array (up to 64kHz) + electrical current
2
NASA IMS
.txt tab-separated
File without headers, written every 10 minutes, 20,480 vibration rows/file
3
NASA CMAPSS
.txt space-separated
26 headerless sensor columns, run-to-failure cycle
› › ›
Normalize to Table Schema → raw_sensor_data
06
PredictaGuard · Project ASTRA

## Slide 8
04 · CLEANING & FEATURE PIPELINE
Cleaning Pipeline — 5 Automated Stages / 30 Seconds
1
Remove Timestamp
Duplications
›
2
Physical
Clipping → NULL
›
3
Adaptive Imputation
(interpolate/ffill)
›
4
Time
Synchronization (round 1s)
›
5
Butterworth
Low-Pass Filter
Physical Limit Thresholds
Temperature
0°C – 200°C
Vibration
-50 – 50 mm/s
Motor Current
0 – 100 A
Imputation based on % missing data: <30% interpolation, 30–70% forward-fill, >70% left as NULL (sensor disconnected).
07
PredictaGuard · Project ASTRA

## Slide 9
04 · CLEANING & FEATURE PIPELINE
Feature Engineering — 25 Features / 30-Second Window
Statistical Features
temp_mean, temp_slope, current_mean, rpm_mean, torque_mean, etc.
Mean/std indicate shifts in baseline load; slope captures the linear heating trend.
Signal-based Features
vib_rms, vib_kurtosis, vib_crest, vib_fft_low/high, current_thd
Kurtosis is sensitive to impulsive spikes from bearing cracks; FFT separates low vs high-frequency patterns.
Cross-parameter Features
load_ratio, temp_per_load, power_estimate
Combines mechanical & electrical parameters to monitor motor efficiency anomalies.
08
PredictaGuard · Project ASTRA

## Slide 10
04 · CLEANING & FEATURE PIPELINE
Domain Knowledge Highlights
Q
Why is Kurtosis important for Bearing Faults?
In the early stages of bearing degradation, the vibration signal is dominated by short-duration sharp impact impulses. RMS has not changed much, but Kurtosis spikes sharply (> 3) — providing early warning weeks before failure.
Q
Why are Cross-Parameter Features important?
Temperature rise can be caused by increasing production loads, not damage. With the temperature-to-current ratio (temp_per_load), we can distinguish natural temperature rises from those indicating cooling issues or bearing friction.
09
PredictaGuard · Project ASTRA

## Slide 11
05 · MODEL ARCHITECTURE
3 Parallel Machine Learning Models
Feature Windows
(120 × 25 sequence)
›
Model A1 — Anomaly Detection
LSTM Autoencoder — Unsupervised
Model A2 — Fault Classification
Gradient Boosting — Supervised
Model B — RUL Prediction
LSTM Regressor — Supervised
›
Decision
Engine
›
Dashboard
/ API /
Notifications
Every 5 minutes, the scheduler fetches the last 120 rows from feature_windows (≈ 1 hour of history) per motor, builds them into a sequence, and runs all three models in parallel. The output of each model (anomaly score, fault type + confidence, RUL days) is combined by the Decision Engine into a single operational decision.
10
PredictaGuard · Project ASTRA

## Slide 12
05 · MODEL ARCHITECTURE
Model A1 — Anomaly Detection
A1
LSTM Autoencoder — unsupervised learning.
Trained solely on healthy machine data.
Encoder compresses sequence (120,25) into a low-dimensional bottleneck, then Decoder reconstructs the original signal.
If the machine begins to degrade, signals deviate from the healthy pattern → high reconstruction error (MSE).
If error exceeds a dynamic threshold → status is flagged as Anomaly.
> 95%
Target Recall — prevents missed faults
> 90%
Target Precision — suppresses false alarms
11
PredictaGuard · Project ASTRA

## Slide 13
05 · MODEL ARCHITECTURE
Model A2 — Fault Classification
A2
Gradient Boosting Classifier — supervised learning.
Runs conditionally (only invoked if Model A1 flags an anomaly).
The model processes the last timestep data to classify the specific failure type.
Categories: healthy, inner_race_fault, outer_race_fault, roller_fault, cavitation, overload, seal_leak, nozzle_blockage.
> 92%
Target Accuracy on labeled test data
> 90%
Target F1-Score (weighted)
12
PredictaGuard · Project ASTRA

## Slide 14
05 · MODEL ARCHITECTURE
Model B — RUL Prediction
B
LSTM Regressor unidirectional, 2-layer, trained using CMAPSS degradation data.
Uses Asymmetric Loss Function (NASA competition scoring).
Late Prediction (late prediction) is penalized much more heavily than Early Prediction, as late prediction risks sudden failure during active production.
Chart: Ilustrasi Penurunan RUL
| W1 | W2 | W3 | W4 | W5 | W6 | W7 | W8
RUL (hari) | 125 | 118 | 100 | 78 | 55 | 30 | 14 | 5
Target Metrics
MAE < 10 cycles · RMSE < 15 cycles
Already achieved in initial validation: MAE 9.93 (PredictaGuard reference).
13
PredictaGuard · Project ASTRA

## Slide 15
06 · DECISION ENGINE
Severity Matrix — Combining 3 Model Outputs
Anomaly
Detected?
No
›
Yes
›
NORMAL
RUL Model B
>= 7 days → WARNING
< 7 days → CRITICAL
WARNING
anomaly_score > 0.65 and RUL 3–7 days
Schedule maintenance during this week when production loads are low.
CRITICAL
anomaly_score > 0.85 and RUL < 3 days, or absolute RUL < 3 days
Inspect immediately — shutdown risk. Schedule emergency maintenance.
NORMAL — outside the above conditions
Recommendation: "Continue routine monitoring." The Decision Engine evaluates conditions sequentially and takes the first matching rule, ensuring every motor always has one clear status and recommendation.
14
PredictaGuard · Project ASTRA

## Slide 16
06 · DECISION ENGINE
False Alarm Handling (Suppression & Moderation)
1
Post-Maintenance Bedding-in
Recently repaired motor (< 24 hours) often shows vibration spikes from installation adaptation → downgraded to NORMAL.
2
High Production Load Scaling
Under maximum production load, natural rises in temperature & current are expected → thermal/current anomalies suppressed to NORMAL.
3
Room/Ambient Temperature Shift
If all motors experience temperature anomalies simultaneously → HVAC issue indicator, status downgraded to WARNING.
4
Transient Startup/Shutdown
Current & vibration spikes during start/stop are read from sharp RPM fluctuations to suppress false alarms.
5
Persistence Trend Check
Spikes occurring in only 1 window without subsequent rising trends are filtered out as transient noise.
15
PredictaGuard · Project ASTRA

## Slide 17
07 · SYSTEM ARCHITECTURE
End-to-End Data Flow
Machine
Sensors (1-Hz)
›
PostgreSQL
raw_sensor_data
›
Scheduler Job 1
(30 seconds)
Cleaning + Feature
›
Scheduler Job 2
(5 minutes)
3 Parallel Models
›
Decision
Engine
›
Dashboard /
Notifications
Notification Trigger Flow
If the Decision Engine assigns WARNING or CRITICAL severity, the system automatically triggers the alarm endpoint which dispatches Email (SMTP) and WhatsApp (Twilio) notifications to relevant technicians, while the dashboard fetches the latest status & predictions via the REST API.
16
PredictaGuard · Project ASTRA

## Slide 18
07 · SYSTEM ARCHITECTURE
Automation Layer & API Endpoints
FastAPI + APScheduler
FastAPI provides REST API for frontend communication & telemetry data ingestion.
Job 1 (30 seconds): pull raw_sensor_data → execute Cleaning & Feature Engineering → save to feature_windows.
Job 2 (5 minutes): fetch last 120 rows → run 3 parallel models → Decision Engine → save to prediction_results.
Method | Endpoint | Description
POST | /api/telemetry | Receive raw 1-Hz sensor data
GET | /api/dashboard/overview | Health overview of all motors and active alarms
GET | /api/predictions/{motor_id} | Latest prediction, RUL, SHAP contributions
POST | /api/work-orders | Create work orders and assign technicians
GET | /api/notifications/settings | Credentials for SMTP email & Twilio WhatsApp gateways
17
PredictaGuard · Project ASTRA

## Slide 19
08 · DASHBOARD
Dashboard Page Flow
Login Screen (Clearance Authentication)
1. Overview
Dashboard
›
2. Machine
Monitoring (Grid of 6)
›
3. Machine Detail
(Live Waveform)
6. Notification
Settings
‹
5. Work Order CRUD
(Assign Technician)
‹
4. Prediction &
Diagnosis (SHAP, RUL)
↑ back to Overview
18
PredictaGuard · Project ASTRA

## Slide 20
08 · DASHBOARD
3 Most Representative Main Pages
1
Overview Dashboard
Factory status cards (number of faulty motors, OEE)
Unified Machine Health Grid — 6 motor panels
Recent Critical Notifications Alert Bar
2
Machine Detail
Interactive selector between motors
Real-time waveform: vibration, current, temperature, RPM
Physical limit gauges (radial dial)
3
Prediction & Diagnosis
RUL status card + historical degradation curve
SHAP feature contribution chart
Maintenance recommendation & work order console
19
PredictaGuard · Project ASTRA

## Slide 21
09 · VALIDATION & TESTING
End-to-End Simulation & 4 Testing Scenarios
End-to-End Simulation — system runs 1 hour nonstop: sensors inject 1-Hz telemetry, scheduler runs cleaning (30s) & inference (5 mins) repeatedly to validate stability and latency.
Scenario 1
Normal
TEST
Healthy telemetry within normal limits
RESULT
NORMAL status, no alerts, RUL ≈ 125 days
Scenario 2
Degradation
TEST
Parameters drift upward slowly
RESULT
WARNING status, scheduled service recommendation
Scenario 3
Sudden Fault
TEST
Extreme vibration, sharp current rise, RUL < 3 days
RESULT
CRITICAL status, WA & Email alerts dispatched < 30 seconds
Scenario 4
Dirty Data
TEST
Flatline, massive nulls, extreme outliers
RESULT
WARNING: sensor malfunction, not mechanical failure
20
PredictaGuard · Project ASTRA

## Slide 22
09 · VALIDATION & TESTING
Field Technician Feedback Loop
1
Predictions &
Work Orders
›
2
Technician
Field Confirmation
›
3
Stored in
Feedback Database
›
4
Retraining Model
(if errors accumulate)
Every time a technician completes a work order, they confirm the actual field conditions: Yes, Accurate / No, False Alarm / Misclassified.
This confirmation is stored in the database as additional ground truth.
If misclassifications accumulate, the system alerts the AI administrator to trigger automated model retraining using the latest historical data with corrected labels.
21
PredictaGuard · Project ASTRA

## Slide 23
10 · CLOSING
Value Proposition & Current System Limitations
VALUE PROPOSITION
1
Minimal Downtime
Shifts the reactive paradigm to predictive — reducing unplanned downtime by 40–50%.
2
Cost Avoidance
Prevents secondary damage & ensures spare parts replacement is done on time.
3
Human Trust Empowerment
Eliminates the "Black Box AI" skepticism through transparent SHAP explanations and clear spare part recommendations.
CURRENT SYSTEM LIMITATIONS
Simulated Environment
Real-world historical breakdown data from the ASTRA plant is still scarce, so the models are currently trained on simulated/transfer learning from public datasets (Paderborn, IMS, CMAPSS).
Threshold Calibration
Current anomaly thresholds use standard statistical parameters, whereas each motor has a unique baseline vibration signature in the field.
22
PredictaGuard · Project ASTRA

## Slide 24
10 · CLOSING
Next Steps — Action Plan Roadmap
1
Months 1–2
Real-world Baseline Data Collection
Install sensors on active ASTRA motors & record normal operating data for 1 month for baseline vibration/thermal profiles.
2
Month 3
Model & Threshold Re-calibration
Fine-tune the LSTM Autoencoder with normal ASTRA data, adjusting anomaly thresholds per machine unit.
3
Months 4–6
Internal CMMS / ERP Integration
Connect the PredictaGuard API to the warehouse logistics system to automate spare parts ordering when RUL is critical.
23
PredictaGuard · Project ASTRA

## Slide 25
Thank You
PredictaGuard — Turning Reactive Maintenance into Resilient Operations.
Project ASTRA · Predictive Maintenance System